## Slide 1: Audio Spotlight
Joon Ki Hong

## Slide 2: What is it?
Audio Spotlight is a directional sound technology developed by Dr. Joseph Pompei of Holosonics.
Focuses audible sound in a specific direction using ultrasound similar to how a flashlight shines light compared to a light bulb.
Used in various ways today specifically in large venues and markets.
Notes: Audio Spotlight is a directional sound technology developed by Dr. Joseph Pompei of Holosonics and developed this technology at MIT as part of his PhD thesis. Holosonics doesn’t consider themselves a sound company but rather a company that adds sounds to preserve the quiet.
It focuses audible sound in a specific direction using ultrasound similar to how a flashlight shines light differently than a light bulb as opposed to the omnidirectional sound conventional speakers produce. This technology is mainly used to isolate noise into a specific region.
It’s used in various ways today, specifically in museums, theme parks such as Disney World, billboards in Manhattan, super markets, and advertisements.

## Slide 3: Some History
U.S Navy used ultrasonic technology (SONAR) to map the sea floor and detect large objects underwater
In the 1960’s researchers developed a SONAR system focused on one particular area.
They also developed equations describing the propagation of sound in water.
The technology was further developed in 1975.
The 1980’s saw the publication of audio spotlight-like technology. It was abandoned.
Notes: Some history on ultrasound technology
The U.S Navy was one of the early adopters of ultrasonic technology in the early 1900’s. They used SONAR to map the sea floor and detect large objects underwater.
Two researchers, Dr. Peter J. Westervelt and Dr. Orhan Berktay developed a SONAR system that focused on one particular area as opposed to every direction.
They also developed a mathematical formula that calculated the distortion of sound within water.
The technology was further developed in 1975 when researchers were able to create audible sounds from a combination of high frequency sounds.
In the 1980’s a team led by Masahide Yoneyama and Jun-ichiroh Fujimoto published a paper on audio spotlight technology and its theoretical results. It was ultimately abandoned due to the unrealistic commercial costs as well as high levels of distortion.

## Slide 4: Two Spotlight Technologies
Dr. Joseph Pompei at Holosonics further developed the Audio Spotlight technology.
Elwood Norris of the American Technology Corporation in California created the HSS.
Both technologies are based on similar concepts.
Notes: Dr. Joseph Pompei at Holosonics further developed the Audio Spotlight technology coined by the Japanese scientists in their publication.
Elwood Norris of the American Technology Corporation in California created the HSS of the Hypersonic Sound.

## Slide 5: So.. How does it work?
Ultrasounds? Why?
Large surface speakers
Audio Spotlight speakers use transducers to create a narrow ultrasonic wave modulated by a mathematical formula to account for distortion in air.
Speaker size to wavelength relationship:
http://www.holosonics.com/tech_directivity.html
Notes: Ultrasounds are defined to be sounds that have frequencies past the upper limit of the human hearing range generally accepted to be past the 20khz range. But if they’re imperceptible to humans why use ultrasounds? Well, because ultrasounds have very short wavelengths they can propagate in a narrow beam.
This is of course dependent on the size of the speaker. There is a physical limitation to speaker directivity in that the directivity is affected by the physical size of the speaker and the wavelengths it’s producing. So by using ultrasounds we can maximize our directivity.
So Audio Spotlight speakers emit these ultrasounds but they’re still inaudible to humans. Well ultrasounds distort as they propagate in air. What Dr. Pompei did was that he created a mathematical formula to predict these distortions in air similar to how the Japanese scientists formulated the propagation of sound in water. Using this formula he was able to backwards engineer the ultrasounds so that the individual within the spotlight of the wave will hear an audible sound that literally forms midway from the transducer to the individual.

## Slide 6: Some Imperfections
Directional Sound technologies are unable to produce bass sounds.
The sounds propagate past the individual and on.
  Evident in Chryslers implementation
Notes: Directional sound technologies unfortunately are unable to produce low frequencies in the same way it can with higher frequencies.
Secondly, the waves can propagate past the individual and reflect off a hard surface and thus remove the isolated effect of the technology.
Chrysler had installed Audio Spotlight in one of their vehicles to provide each passenger with their own private radio. However, the sounds were reflecting off the leather and interior of the car which then allowed other passengers to hear each others music.

## Slide 7: A Few Demonstrations
Art Piece
Troll [0:20]
Mozart Demo [3:48]

## Slide 8: Sources
http://www.holosonics.com/tech_directivity.html
http://en.wikipedia.org/wiki/Sound_from_ultrasound
http://www.researchusa.org/play.php?vid=844
http://commlaw.cua.edu/articles/v17/17.1/Bankey.pdf
http://electronics.howstuffworks.com/gadgets/high-tech-gadgets/brain-advertisement1.htm
http://mesoscopic.mines.edu/mediawiki/images/7/72/Yoneyama_spotlight_83.pdf